Temporary Exemptions Report

Melbourne Metropolitan Railway

Reporting Period: 9 June 2022 – 8 June 2023

Contents

Introduction	4

Transport Standards section 2.1: Unhindered passage	5

Temporary exemption: existing rail premises and existing rail infrastructure	5

For a period of 5 years, flange gaps of up to 75mm are permitted where a level crossing forms part of an access path on existing rail premises or existing rail infrastructure.	5

Reporting Requirements:	5

a)	Findings of audit of flange gaps (clause 1(a))	5

b)	Strategy demonstrating proposed actions (clause 1(b))	5

c)	Proposed time frames (clause 1(c))	9

d)	Proposed expenditure (clause 1(d))	10

Premises Standards H2.2: Accessways	11

Temporary exemption: existing rail premises and existing rail infrastructure	11

For a period of 5 years, flange gaps of up to 75mm are permitted where a level crossing forms part of an accessway on existing rail premises or existing rail infrastructure.	11

Reporting Requirements:	11

a)	Findings of audit of flange gaps (clause 1(a))	11

b)	Strategy demonstrating proposed actions (clause 1(b))	11

c)	Proposed time frames (clause 1(c))	11

d)	Proposed expenditure (clause 1(d))	11

Transport Standards section 2.6: Access paths - conveyances	12

Temporary exemption: existing rail conveyances	12

For a period of 5 years, an access path is only required at a single door of existing rail conveyances.	12

Reporting Requirements:	12

a)	Signage installation (clause 2)	12

b)	Confirmation of signage installation completion (clause 3)	12

c)	Strategy demonstrating intention to provide access paths (clause 5)	13

d)	Progress report (clause 6)	14

Transport Standards section 2.8: Extent of path	14

Temporary exemption: existing rail conveyances	15

For a period of 5 years, an access path is only required at a single door of existing rail conveyances.	15

Reporting Requirements:	15

a)	Confirmation of signage installation completion (clause 3)	15

b)	Strategy demonstrating intention to provide access paths (clause 5)	15

c)	Progress report (clause 6)	15

Transport Standards section 6.4: Slope of external boarding ramps	16

Temporary exemption: existing rail conveyances	16

For a period of 5 years, for existing rail conveyances, where the relationship between the platform and rail carriage means that an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4, ARA members are not required to provide staff assistance in ascending or descending the ramp.	16

Reporting Requirements:	16

a)	Data mapping (clause 1 (a))	16

b)	Written strategy (clause 1 (b))	16

c)	Safety management plan (clause 1 (c))	17

Transport Standards section 8.2: When boarding devices must be provided	19

Temporary exemption: existing rail conveyances	19

For a period of 5 years, a manual or power assisted boarding device is only required at a single door of an existing rail conveyance.	19

Reporting Requirements:	19

a)	Conveyance number and relevant mode of rail travel (clause 4 (a))	19

b)	Number of Stations (clause 4 (b))	19

c)	Information measures (clause 4 (c))	19

d)	Safety and staff training (clause 4 (d))	20

e)	Passenger assistance measures (clause 4 (e))	21

Annexure 1: relevant sections of the Transport Standards and Premises Standards	22

Appendix A – Acronyms, abbreviations and glossary	25

Appendix B – Pedestrian crossings forming part of station access paths where flange gaps at level crossings are identified as non-compliant	26

Appendix C – Stations with Curved Platforms	29

Appendix D – DSAPT Section 6.4 Slope of external boarding ramps	31

Introduction

The Melbourne metropolitan railway network (Network) currently comprises:

- 17 lines;

- 221 stations with 497 platforms;

- Four electric train types, comprising:

  - 115 Comeng units;

  - 72 Siemens Nexas units;

  - 212 X’Trapolis units; and

  - 51 High Capacity Metro Trains units, and

- Two diesel operated Sprinter trains on the Stony Point line.

Head, Transport for Victoria (Head, TfV), established under the Transport Integration Act 2010 (Vic), is a body corporate responsible for managing the Network on behalf of the State of Victoria.

Pursuant to a Franchise Agreement – Train between Head, TfV and Metro Trains Melbourne Pty Ltd (Metro) dated 2 October 2017, Metro is the operator of the Network.

Metro is a member of the Australasian Railway Association (ARA).

On 9 June 2022, the Australian Human Rights Commission (AHRC) granted temporary exemptions to members of the ARA in relation to various provisions of the Disability Standards for Accessible Public Transport 2002 (Cth) (Transport Standards) and the Disability (Access to Premises – Buildings) Standards 2010 (Cth) (Premises Standards).

Metro provides this document in relation to the Network and the applicable temporary exemptions which contain reporting and strategy requirements.

Should you have any feedback in relation to this report, please contact:

Phone (free call):	1800 800 007 – Department of Transport and Planning

6am to midnight daily (all night on Fridays & Saturdays)

Email:	http://www.metrotrains.com.au/customer-feedback/

Website:	www.metrotrains.com.au

Postal address:	Metro Trains Melbourne Pty Ltd

Customer Feedback

GPO Box 1880

MELBOURNE VIC 3001

Transport Standards section 2.1: Unhindered passage

Temporary exemption: existing rail premises and existing rail infrastructure

For a period of 5 years, flange gaps of up to 75mm are permitted where a level crossing forms part of an access path on existing rail premises or existing rail infrastructure.

Reporting Requirements:

- Findings of audit of flange gaps (clause 1(a))

Condition - The ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out the findings of the audit, including identifying each station where a level crossing forms part of an access path and, for each location, the nature of the non-compliance and the mode of rail travel so that the member may achieve compliance with the Transport Standards by the end of the exemption period.

Response - A desktop audit of existing datasets identified each station where a pedestrian level crossing forms part of an access path and, for each location, the nature of the non-compliance.  The methodology used to prepare this audit utilises a collation of all available data from the Level Crossing Management System (LXM) as of April 2023 and from internal Metro departments to understand the outstanding non-compliances with the exemption. The full list of identified pedestrian crossings forming part of station access paths is documented in Appendix B.

- Strategy demonstrating proposed actions (clause 1(b))

Condition - The ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out a strategy demonstrating the proposed actions for remedy in each location identified in the audit by:

- eliminating the flange gaps with a suitable product;

- reducing the flange gaps to a maximum horizontal width of 55mm; or

- phasing out by grade separation,

so that the member may achieve compliance with the Transport Standards by the end of the exemption period.

Response (i) and (ii) - Elimination of Flange Gaps with Suitable Product and Reduction of Flange Gaps to a maximum horizontal width of 55mm

Background

VeloSTRAIL is a rubber panel pedestrian crossing system that eliminates the flange gaps. VeloSTRAIL is similar to the previously used PedeSTRAIL, the key difference is a compressible, replaceable rubber flangeway element that fills the flangeway gap between the rail profile and level crossing surface, which provides the gap-free solution.

In 2018, Metro has installed the VeloSTRAIL 47 at Keon Parade, Keon Park for trial and monitoring and is currently still in-service.  It was reported that the grease-resistant wear parts were effective at keeping wheel flange lubrication away from the surface groove, however it caused grease deposition on the underside of the panel. Further site inspections identified that the renewed flangeway elements showed excessive signs of deterioration caused by rail lubrication and had to be replaced.

In April 2023, the VeloSTRAIL 47 was provisionally approved to be installed at the Diamond Creek and Montmorency pedestrian crossings. Metro is closely monitoring a slip resistance non-compliance due to the adoption of the VeloSTRAIL gap filler. In accordance with Metro’s standards, in areas with pedestrian access the minimum slip resistance classification of P5 or R12 is to be achieved as per AS 4586. The slip resistance will be monitored as part of the trial and further investigation will be undertaken with the manufacturer. The provisional type approval of the VeloSTRAIL 47 expires June 2024 with several trial success criteria addressing the flangeway element deterioration and accumulation of railway lubrication. At the conclusion of the trial period, an evaluation report to assess the product’s performance based on the trial success criteria will be reviewed as part of the type approval process. It is noted that there is no known product is available on the market that both minimises the flange gap and has a compliant slip resistant rating.

Strategy and Limitations

The VeloSTRAIL system supports a maximum train traversing speed of 120km/h. The Network supports regional passenger railway services which exceed these limits and currently would not allow for installation of this product. This limitation would not allow the product to be suitable at the following pedestrian crossings:

Table 1 Pedestrian Crossing on Rail Line Speed >120km/h

| Pedestrian Crossing | Access to Station |
| --- | --- |
| Waratah Street, Altona | Seaholme Station |
| Pier Street, Altona | Altona Station |
| Maidstone Street, Altona | Westona Station |
| Old Calder Highway, Diggers Rest | Diggers Rest Station |
| Down end of Platform Craigieburn, Craigieburn | Craigieburn Station |

As of May 2023, there is also currently no fully type approved product to remove or minimise flange gaps on the Network. Locations nominated for VeloSTRAIL installation trial shall be risk assessed with consideration given to availability and suitability of parts on curves of less than 350m, proximity to rail lubricators and potential vandalism. Upon full type approval of the product, it is recommended for Department of Transport and Planning (DTP) to review the options proposed and initiate a formal development process as the next step to address flange gaps on pedestrian access paths. Any type approval may include conditions which will not allow for the product to be installed at all pedestrian crossings. Individual sites will be assessed for suitability.

Table 2 Proposed timeframes and expenditure for the Flange Gap Product Solution

| Proposed Strategy Actions (1) | Proposed Timeframe | Estimated Expenditure |
| --- | --- | --- |
| Joint inspection by installer and infrastructure maintainer | Every 3 months until June 2024 | - |
| Type Approval Evaluation Report based on Trial Success Criteria | Within 6 months after the trial period | - |
| Installation of suitable flange gap reduction product - 1no. location over 2 tracks | Within 2 years of contract award, or otherwise agreed in project contract. | $ 105,000(2)(3) |

Note:
(1)	Listed actions may only be completed in the listed order.

(2)	Proposed cost does not include occupation cost.

(3)	Proposed cost is indicative and for guidance only, subject to change.

Response (iii) - Phase out by Grade Separation

Metro is a member of the Victorian Railway Crossing Safety Steering Committee (VRCSSC) and the subgroup Railway Crossing Safety Delivery Group (RCSDG), continues to support Victorian Railway Level Crossing Safety Strategy and the associated action plans.

The flange gap non-compliance may be phased out by grade separation which has in most recent years been combined with the building of a new rail-under or rail-over station with new accessible pathways. Metro recognises grade separation to be the only fully compliant solution to flange gaps forming part of an access path.

Metro as a key stakeholder and alliance delivery partner in all Level Crossing Removal Projects (LXRP) within the Melbourne Network has successfully delivered 65 level crossing removals as part of the LXRP program.  Metro will continue to deliver the following pedestrian crossings removals which have been committed for grade separation.

Table 3 List of Pedestrian Crossings within the LXRP wider Scope of Works

| Pedestrian Crossing, Suburb | Access to Station | Delivery Timeframe | Expenditure |
| --- | --- | --- | --- |
| Glen Huntly Road, Glen Huntly | Glenhuntly Station | By 2023 | $507 million; Packaged with Glen Huntly Road and Neerim Road LXRP scope |
| Main Street, Pakenham | Pakenham Station | By 2024 | $844 million; Packaged with Main Street, McGregor Road and Racecourse Road LXRP scope |
| UeoP Pakenham, Pakenham |  |  |  |
| Keon Parade, Keon Park | Keon Park Station | By 2025 | $277 million; Packaged with Keon Parade LXRP scope |
| Alameda St/Bethell Ave, Parkdale | Parkdale Station | By 2025 | $450 million; Packaged with Warrigal Road and Parkers Road LXRP scope |
| Parkers Road, Parkdale |  |  |  |
| Up end of Platform East Ringwood, Ringwood East | Ringwood East Station | By 2025 | $572 million; Packaged with Dublin Road, Coolstore Road and Cave Hill Road LXRP scope |
| Down end of Platform East Ringwood, Ringwood East |  |  |  |
| Up end of Platform Croydon, Croydon | Croydon Station | By 2025 |  |
| Kent Avenue, Croydon |  |  |  |
| Webb Street, Narre Warren | Narre Warren Station | By 2025 | $259 million; Packaged with Webb Street LXRP scope |
| Barkly Street, Brunswick | Jewell Station | By 2030 | To be packaged by LXRP |
| Union Street, Brunswick |  |  |  |
| Albert Street, Brunswick | Brunswick Station | By 2030 | To be packaged by LXRP |
| Victoria Street, Brunswick |  |  |  |
| West Street, Brunswick | Anstey Station | By 2030 | To be packaged by LXRP |
| Albion Street, Brunswick |  |  |  |
| Highett Road, Highett | Highett Station | By 2030 | To be packaged by LXRP |
| Station Street, Seaford | Seaford Station | By 2030 | To be packaged by LXRP |
| McDonald Street, Mordialloc | Mordialloc Station | By 2030 | To be packaged by LXRP |
| Bear Street, Mordialloc |  |  |  |
| Anderson Street, Yarraville | Yarraville Station | By 2030 | To be packaged by LXRP |
| Hudsons Road, Spotswood | Spotswood Station | By 2030 | To be packaged by LXRP |

Grade separation of the pedestrian crossings forming part of a station access path not listed in Table 3 above may be achieved by:

- Installation of pedestrian overpass; or

- Installation of pedestrian underpass.

The proposed timeframes and expenditure are heavily reliant on the scope included in the grade separation of the pedestrian crossing.

| Scope of Works | Proposed Timeframe | Estimated Expenditure |
| --- | --- | --- |
| Pedestrian Overpass Solution (Bridge & ramps, no lifts) | Within 2 years of contract award, or otherwise agreed in project contract. | $15 million - $25 million (2)(3)(4)(5) |
| Pedestrian Underpass Solution | Within 2 years of contract award, or otherwise agreed in project contract. | $20 million - $35 million (2)(3)(4)(5) |

Note:
(2)	Proposed cost does not include occupation cost.

(3)	Proposed cost is indicative and for guidance only, subject to change.

(4)	Proposed cost does not include owners’ costs (land acquisition, other Owner Development costs etc).

(5)	Proposed cost does not include rail systems, track and electrical networks scope of works.

- Proposed time frames (clause 1(c))

Condition - the ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out the proposed time frames for the remedy in each location so that the member may achieve compliance with the Transport Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 1(b) (strategy demonstrating proposed actions), condition 2.1 (Unhindered passage).

- Proposed expenditure (clause 1(d))

Condition - the ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out the proposed expenditure to remedy each location so that the member may achieve compliance with the Transport Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 1(b) (strategy demonstrating proposed actions), condition 2.1 (Unhindered passage).

Premises Standards H2.2: Accessways

Temporary exemption: existing rail premises and existing rail infrastructure

For a period of 5 years, flange gaps of up to 75mm are permitted where a level crossing forms part of an accessway on existing rail premises or existing rail infrastructure.

Reporting Requirements:

- Findings of audit of flange gaps (clause 1(a))

Condition - the ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out the findings of the audit, including identifying each station where a level crossing forms part of an accessway and, for each location, the nature of the non-compliance and the mode of rail travel so that the member may achieve compliance with the Premises Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 1(a) (findings of audit of flange gaps), condition 2.1 (Unhindered passage).

- Strategy demonstrating proposed actions (clause 1(b))

Condition - the ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out a strategy demonstrating the proposed actions for remedy in each location identified in the audit by:

i.	eliminating the flange gaps with a suitable product;

ii.	reducing the flange gaps to a maximum horizontal width of 55mm; or

iii.	phasing out by grade separation,

so that the member may achieve compliance with the Premises Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 1(b) (strategy demonstrating proposed actions), condition 2.1 (Unhindered passage).

- Proposed time frames (clause 1(c))

Condition - the ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out the proposed time frames for the remedy in each location so that the member may achieve compliance with the Premises Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 1(b) (strategy demonstrating proposed actions), condition 2.1 (Unhindered passage).

- Proposed expenditure (clause 1(d))

Condition - the ARA member concerned conducts an audit of flange gaps at existing crossings against s 2.1 of the Transport Standards and cl H2.2 of the Access Code in the Premises Standards and provides a written report to the ARA and the Commission within 12 months setting out the proposed expenditure to remedy each location so that the member may achieve compliance with the Premises Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 1(b) (strategy demonstrating proposed actions), condition 2.1 (Unhindered passage).

Transport Standards section 2.6: Access paths - conveyances

Temporary exemption: existing rail conveyances

For a period of 5 years, an access path is only required at a single door of existing rail conveyances.

Reporting Requirements:

- Signage installation (clause 2)

Condition - within 12 months of the grant of this exemption, the ARA member utilising this exemption installs signage in close proximity to the primary boarding point to notify passengers with mobility disability how access can be achieved through an alternative entry point, with staff assistance if required.

Response - Metro has consulted passengers in relation to the information they need to assist them with boarding different train types.  Passengers requested that, at first instance, information be provided in relation to the location of the primary boarding point. If an alternative boarding point is required for a particular service, a staff member will greet the passenger at the primary point, and provide information about the alternative boarding point.

The nominated platform boarding point is identified at most stations by a floor decal showing the International Symbol for Access.  Floor decals at the entrance of most platforms direct passengers to the nominated primary boarding point.

| Decal directing passengers to the primary boarding point | Decal identifying the primary boarding point |
| --- | --- |

Station staff are available at some locations to answer passenger queries. Each platform is fitted with a passenger intercom button to the closest control centre. This means passengers who are be unsure of boarding processes at unstaffed stations can also speak to a staff member.

- Confirmation of signage installation completion (clause 3)

Condition – the ARA member utilising this exemption reports to the Commission within 12 months of the exemption confirming the completion of the installation of the signage.

Response - Please see Metro’s response in clause 2 (signage installation), condition 2.6 (access path conveyances).

- Strategy demonstrating intention to provide access paths (clause 5)

Condition - the ARA member utilising this exemption provides a written strategy to the ARA and the Commission within 12 months of this exemption to demonstrate how the member intends to provide access paths between the entrance of a conveyance and the allocated spaces and other essential facilities for passengers with disabilities, including the relevant mode of rail travel, its proposed time frames for actioning this strategy, and proposed expenditure for that action so that the member may achieve compliance with the Transport Standards by the end of the exemption period.

Response - With Metro’s current operating model, the driver is the sole operator of the train. Allocated spaces are provided from the first door of the first carriage, at intermittent points and at the last door of the sixth carriage. The operational demands of network service and punctuality do not allow for the driver to deploy a ramp for the entire length of the train. To maintain operations, additional staffing would be required at each platform on the Network. With over 500 platforms on the Network, this would require an operating cost of $740 million per annum. This is not a desirable strategy as it does not achieve independent travel over time.

Metro has introduced a platform standard which achieves accessible boarding as far possible to allow clearance requirements to prevent platform/conveyance collisions and general maintenance tolerances. These tolerances are required to ensure that the Network can cater for the different train types, which includes freight.

While the standard, which includes rubber platform gap fillers, has proven to achieve independent boarding, it does not meet the prescribed tolerances within the Transport Standards. The driver remains available should any passenger require assistance. Metro has been progressively upgrading platforms to meet the standard.

Table 4 Strategy actions for improved access paths - conveyances

| Scope of Works | Notes | Proposed Timeframes | Estimated Expenditure |
| --- | --- | --- | --- |
| Raised platform height & installation of platform gap fillers throughout the length of platform (per platform) | Cannot be installed at curved platforms due to platform strike risk. Refer to Appendix C for full list of stations with curved platforms. | Within 2 years of contract award, or otherwise agreed in project contract. | $445,000(2)(3) |
| New Station Rebuild (station with 2no. platform) | For stations with curved platforms, new platform and track alignment required to achieve compliance with Metro standard | Within 3 years of contract award, or otherwise agreed in project contract. | $50 million - $80 million(2)3)(5) |
| Installation of platform gap fillers throughout the length of platform (per platform) | Only at platforms with existing compliant platform height. | Within 2 years of contract award, or otherwise agreed in project contract. | $120,000 (2)(3) |

Note:
(2)	Proposed cost does not include occupation cost.

(3)	Proposed cost is indicative and for guidance only, subject to change.

(5)	Proposed cost does not include rail systems, track and electrical networks scope of works.

- Progress report (clause 6)

Condition – the ARA member utilising this exemption provides reports to the Commission every 12 months from the date of this exemption setting out the member’s progress toward providing access paths between the entrance of a conveyance and all allocated spaces and facilities for passengers with disabilities, including:

(a)	the number of conveyances over which this exemption is claimed and the relevant mode of rail travel;

(b)	the actual expenditure incurred in implementing the strategy in the previous 12 months, expressed as a dollar figure and as a percentage of total budget; and

(c)	the safety procedures and staff training in place to ensure the safe and timely evacuation of people with disability from conveyances in the event that evacuation is required, including in the event of an emergency.

Response -

- Number of conveyances and mode of rail travel

Metro is the operator of Melbourne’s metropolitan rail network. Metro claims this exemption over all the conveyances it operates.

As at May 2023, this included 115 Comeng units, 72 Siemens Nexus units, 212 X’Trapolis units. These trains are primarily operated in service as two coupled units, i.e. as six-car trains. Metro also operates 51 HCMT units, 34 of which are currently in service, as well as two diesel Sprinter trains on the Stony Point line.

- Actual expenditure

Details of expenditure to deliver strategy will be provided for the period of June 2023 – June 2024 to align with Part (c) (above), section 2.6 (access path conveyances).

- Safety procedures and staff training

Evacuations are rare, and the specific circumstances of an incident will guide the staff response and interaction with emergency services.  Emergency management procedures support staff decisions.

In limited circumstances, Metro or emergency services may decide to evacuate passengers at a non-platform location. Decisions to detrain passengers require a careful assessment of the specific circumstances of an incident, and consideration of the assistance required by all impacted passengers. Metro is reliant on the advice of emergency services in an emergency situation.

In a non-emergency situation, Metro will firstly prioritise moving the train to a platform to enable alighting.  If the train is unable to be moved, Metro will wait for assistance from emergency services before detraining non-ambulant passengers.

When detraining takes place at a station platform, Metro staff members can provide direct assistance in a manner similar to a normal station stop, provided doors are operational. If doors are not operational, the consideration will be similar to non-platform incidents, and emergency services may assist.

Frontline staff are trained in detraining and emergency response as applicable to their roles.

Transport Standards section 2.8: Extent of path

Temporary exemption: existing rail conveyances

For a period of 5 years, an access path is only required at a single door of existing rail conveyances.

Reporting Requirements:

- Confirmation of signage installation completion (clause 3)

Condition - the ARA member utilising this exemption reports to the Commission within 12 months of the exemption confirming the completion of the installation of the signage.

Response - Please see Metro’s response in clause 3 (confirmation of signage installation completion) of condition 2.6 (access path conveyances).

- Strategy demonstrating intention to provide access paths (clause 5)

Condition - the ARA member utilising this exemption provides a written strategy to the ARA and the Commission within 12 months of this exemption to demonstrate how the member intends to provide access paths between the entrance of a conveyance and the allocated spaces and other essential facilities for passengers with disabilities, including the relevant mode of rail travel, its proposed time frames for actioning this strategy, and proposed expenditure for that action so that the member may achieve compliance with the Transport Standards by the end of the exemption period.

Response - Please see Metro’s response in clause 5 (Strategy demonstrating intention to provide access paths) of condition 2.6 (access path conveyances).

- Progress report (clause 6)

Condition – the ARA member utilising this exemption provides reports to the Commission every 12 months from the date of this exemption setting out the member’s progress toward providing access paths between the entrance of a conveyance and all allocated spaces and facilities for passengers with disabilities, including:

(a)	the number of conveyances over which this exemption is claimed and the relevant mode of rail travel

(b)	the actual expenditure incurred in implementing the strategy in the previous 12 months, expressed as a dollar figure and as a percentage of total budget, and

(c)	the safety procedures and staff training in place to ensure the safe and timely evacuation of people with disability from conveyances in the event that evacuation is required, including in the event of an emergency.

Response - Please see Metro’s response in clause 6 (progress report) of condition 2.6 (access path conveyances).

Transport Standards section 6.4: Slope of external boarding ramps

Temporary exemption: existing rail conveyances

For a period of 5 years, for existing rail conveyances, where the relationship between the platform and rail carriage means that an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4, ARA members are not required to provide staff assistance in ascending or descending the ramp.

Reporting Requirements:

- Data mapping (clause 1 (a))

Condition - within 12 months of the exemption, the ARA member utilising this exemption undertake data mapping of all stations and stops state-wide to identify the relevant locations where an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4 and provide to the Commission a report setting out its findings from the data mapping, including identifying the locations at which an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4 and the relevant mode of rail travel.

Response - This data mapping identifies the stations at which an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4 and the relevant mode of rail travel. Metro maintenance inspection data available as of April 2023 was used to inform whether compliance for this requirement has been met for each station.

The data mapping is based on the height of the platform at boarding point and the carriage floor height of the Siemens type train running on the Northern Group, Central Group and Caulfield Group stations, and the Comeng type train for the Burnley Group and Clifton Hill Group stations. There are 79 platforms where boarding ramp slopes of 1 in 8 or better cannot be achieved, the full list is documented in Appendix D. The gradient is improved for the X’Trapolis and HCMT train types, which have lower carriage floor heights.

- Written strategy (clause 1 (b))

Condition - within 12 months of the exemption, the ARA member utilising this exemption undertake data mapping of all stations and stops state-wide to identify the relevant locations where an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4 and provide to the Commission a written strategy on how platforms can be improved at nominated boarding points on a case-by-case basis, including time frames for action and planned expenditure for the improvements.

Response - Using a calculation of the vertical height difference of the train and platform, as well as the length of portable boarding ramps, Metro identified minimum works required to achieve a 1 in 8 gradient across platforms on the Network.

For new or upgraded stations, platform height standards will prevent any ongoing non-compliances. This ensures better alignment between platform heights with train floor heights.

For locations identified via data mapping, a solution requires the re-sheeting, re-surfacing, re-tactiling and any required line marking and coping for each platform.

Introduction of raised boarding pads (RBP) and platform gap fillers on various stations on the Network in the recent years has facilitated the development of independent boarding for passengers using wheelchairs, allowing independent access to trains without the provision of a ramp.

Installation of RBPs may prohibit some V/line services travelling through these locations due to the change in clearances which platform strikes. Speed restrictions may also be required to be imposed on Heritage and V/line running lines which will impact on timetables and scheduling, causing restrictions by delaying services.

Metro has completed platform works and made platforms compliant through several ongoing projects:

- Platform Gap Mitigation Project

- Better Stations

- Annual Infrastructure Renewal Works

Identified locations which do not allow for a 1 in 8 portable ramp or better are available for passengers on the Accessibility Guide on the Metro website.

The following stations are currently in project delivery for station upgrade works:

- Clifton Hill

- Croydon

- Essendon

- Glen Huntly

- Glen Waverley

- Lalor

- Macleod

- Merri

- Moonee Ponds

- Pakenham

- Ringwood East

- Thornbury

- Victoria Park

Proposed Timeframes and Expenditure

Stations being completed or proposed level crossings removal projects were also removed from the list to be costed but for, stations (where to the best of our Metro SME’s knowledge), the proposed gap to compliance has not or is not envisaged to be met in the future as part of the known scope. The costed solution has been based on the construction of a platform height to achieve a compliant ramp gradient based on previous costings. This solution requires the re-sheeting, re-surfacing, re-tactiling, line marking and coping for each platform and may require track realignment.

Table 5 Strategy actions for improved external boarding ramp

| Scope of Works | Proposed Timeframe | Estimated Expenditure |
| --- | --- | --- |
| Installation of raised boarding pad (per platform) | Within 2 years of contract award, or otherwise agreed in project contract. | $200,000(2)(3) |
| Platform Resurfacing (per platform) | Within 2 years of contract award, or otherwise agreed in project contract. | $325,000(2)(3) |
| Platform Resurfacing & track realignment (2 no. platforms and full pit renewal) | Within 2 years of contract award, or otherwise agreed in project contract. | $3.3million - $5.5million(2)(3) |

Note:
(2) Proposed cost does not include occupation costs.

(3) Proposed cost is indicative and for guidance only, subject to change.

- Safety management plan (clause 1 (c))

Condition - within 12 months of the exemption, the ARA member utilising this exemption undertake data mapping of all stations and stops state-wide to identify the relevant locations where an external board ramp can only be provided at a gradient greater than 1 in 8 and less than 1 in 4 and provide to the Commission a safety management plan addressing the safety procedures and staff training in place to ensure the safe and timely evacuation of people with disability from conveyances at these locations in the event that evacuation is required, including during an emergency.

Response - Evacuations are rare, and the specific circumstances of an incident will guide the staff response and interaction with emergency services.  Emergency management procedures support staff decisions.

In limited circumstances, Metro or emergency services may decide to evacuate passengers at a non-platform location. Decisions to detrain passengers require a careful assessment of the specific circumstances of an incident, and consideration of the assistance required by all impacted passengers. Metro is reliant on the advice of emergency services in emergency situations.

In a non-emergency situation, Metro will firstly prioritise moving the train to a platform to enable alighting.  If the train is unable to be moved, Metro will wait for assistance from emergency services before detraining non-ambulant passengers.

When detraining takes place at a station platform, Metro staff members can provide direct assistance in a manner similar to a normal station stop, provided doors are operational. If doors are not operational, the consideration will be similar to non-platform incidents, and emergency services may assist.

Frontline staff are trained in detraining and emergency response as applicable to their roles.

Transport Standards section 8.2: When boarding devices must be provided

Temporary exemption: existing rail conveyances

For a period of 5 years, a manual or power assisted boarding device is only required at a single door of an existing rail conveyance.

Reporting Requirements:

- Conveyance number and relevant mode of rail travel (clause 4 (a))

Condition – any ARA member utilising the exemption provides a report to the Commission and the ARA within 12 months of the grant of this exemption on the number of conveyances over which this exemption is claimed, including the relevant mode of rail travel.

Response - Metro claims this exemption over all the conveyances it operates.

As at May 2023, this included 115 Comeng units, 72 Siemens Nexus units, 212 X’Trapolis units. These trains are primarily operated in service as two coupled units, ie as six-car trains. Metro also operates 51 HCMT units, 34 of which are currently in service, as well as two diesel Sprinter trains on the Stony Point line.

- Number of Stations (clause 4 (b))

Condition – any ARA member utilising the exemption provides a report to the Commission and the ARA within 12 months of the grant of this exemption on the number of stations where an assisted boarding device is provided only at a single door of any conveyance consistent with this exemption.

Response - Metro Trains’ network includes 221 stations.

The first set of passenger doors on the front carriage of the train is the primary boarding point for all Metro Trains, regardless of the station. Metro staff members can provide direct assistance at that door, which may include deploying a boarding ramp.

If an alternative boarding point is required - for example, because all wheelchair accessible spaces adjacent to the first door are already in use - the Metro staff member will greet the passenger at the primary boarding point, and assist them to the alternative boarding point. The Metro staff member will then provide direct assistance at that door. Again, this may include deploying a boarding ramp at that door. The location of the alternative boarding door differs depending on train type.

- Information measures (clause 4 (c))

Condition - any ARA member utilising the exemption provides a report to the Commission and the ARA within 12 months of the grant of this exemption on the measures taken to ensure that staff and passengers are adequately informed of:

- the doors of rail conveyances at which boarding devices are available, and

- the equivalent access measures available, including how passengers can signal for assistance from staff at the equivalent access location.

Response - Metro has consulted passengers in relation to the information they need to assist them with boarding different train types.  Passengers requested that, at first instance, information be provided in relation to the location of the primary boarding point. As noted above, if an alternative boarding point is required for a particular service, a staff member will greet the passenger at the primary point, and provide information about the alternative boarding point.

The nominated platform boarding point is identified at most stations by a floor decal showing the International Symbol for Access.  Floor decals at the entrance of most platforms direct passengers to the nominated primary boarding point.

| Decal directing passengers to the primary boarding point | Decal identifying the primary boarding point |
| --- | --- |

Station staff are available at some locations to answer passenger queries. Each platform is fitted with a passenger intercom button to the closest control centre. This means passengers who are be unsure of boarding processes at unstaffed stations can also speak to a staff member.

Passengers can also obtain boarding information from other sources including:

- Metro’s website (see http://www.metrotrains.com.au/accessibility/boarding);

- Travellers Aid Centres;

- education sessions conducted by Metro’s Community Education Unit; and

- education/confidence-building events like Try Before You Ride.

Frontline staff are trained in providing boarding information and assistance as applicable to their roles.

- Safety and staff training (clause 4 (d))

Condition – any ARA member utilising the exemption provides a report to the Commission and the ARA within 12 months of the grant of this exemption on the safety procedures and staff training in place for the safe and timely evacuation of people with disability from conveyances at locations where an assisted boarding device is only provided at a single door of a conveyance in the event of a need to evacuate, including an emergency.

Response - As noted above, when detraining takes place at a station platform, Metro staff members can provide direct assistance in a manner similar to a normal station stop, provided doors are operational. If doors are not operational, the consideration will be similar to non-platform incidents discussed above, and emergency services may assist.

Frontline staff are trained in detraining and emergency response as applicable to their roles.

- Passenger assistance measures (clause 4 (e))

Condition – any ARA member utilising the exemption provides a report to the Commission and the ARA within 12 months of the grant of this exemption on measures taken to ensure that assistance is provided to passengers at each station at all times the railway is operating, whether by the driver of the conveyance or by ensuring sufficient staff are available at stations to assist passengers through the deployment of the assisted boarding device, the number of staff at each station and the roles in which they are employed, and the planned and actual expenditure incurred in implementing these measures, expressed as a dollar figure and as a percentage of total budget.

Response - To ensure assistance is available to passengers at each station at all times the railway is operating, Metro train drivers provide direct assistance to passengers who require boarding assistance. Conductors on the Stony Point line fulfill this role. This work is done as part of their normal employment duties. As at May 2023, Metro employed 1330 drivers.

In some cases, station staff do also provide this assistance. Metro employs over 1000 station staff, with varying numbers rostered at different stations at various days and times. They fulfill a variety of duties, such as providing customer service, selling tickets, and staffing ticket barriers.

Annexure 1: relevant sections of the Transport Standards and Premises Standards

2.1	Unhindered passage

- An access path that allows unhindered passage must be provided along a walkway, ramp or landing.

- An access path must comply with AS1428.2 (1992) Clause 8.1.

|  | Premises | Infrastructure |
| --- | --- | --- |
|  | except premises to which the Premises Standards apply | except airports that do not accept regular public transport services |

2.6	Access paths — conveyances

- Subject to subsection (3) and section 2.7, an access path that allows continuous and unhindered passage must be provided with a minimum width of at least 850 mm.

- Subsection (1) applies to doorways and stairs, and between entrances, exits, allocated spaces and other essential facilities for passengers using wheelchairs and other mobility aids.

- If the conveyance exists or is ordered before the commencement of this section, the minimum width may be reduced to 800 mm at any doorway restriction.

Conveyances

Buses Ferries Trains Trams Light rail

2.8	Extent of path

- An access path must extend from the entrance of a conveyance to the facilities or designated spaces provided for passengers with disabilities.

- Up to 50 mm of an adjacent allocated space may be used as part of the access path.

- If an access path cannot be provided, the operator must provide equivalent access by direct assistance.

Conveyances

Buses Ferries Trains Trams Light rail

6.4	Slope of external boarding ramps

The slope of an external boarding ramp must not exceed:

(a)	1 in 14 for unassisted access (AS/NZS3856.1 (1998) Clause 2.1.8 (e) (including the notes)); and

(b)	1 in 8 for unassisted access where the ramp length is less than 1520 mm (AS1428.2 (1992) Clause 8.4.2 (a) and AS1428.1 (2001) Figure 8); and

(c)	1 in 4 for assisted access (AS/NZS3856.1 (1998) Clause 2.1.8 (e)).

| Conveyances |  |  |
| --- | --- | --- |
| except dedicated school buses and small aircraft |  |  |

8.2 	When boarding devices must be provided

- A manual or power assisted boarding device must be available at any accessible entrance to a conveyance that has:

(a)	a vertical rise or gap exceeding 12 mm (AS/NZS3856.1 (1998) Clause 2.1.7 (f)); or

(b)	a horizontal gap exceeding 40 mm (AS/NZS3856.1 (1998) Clause 2.1.8 (g)).

Conveyances

except dedicated school buses and small aircraft

H2.2	Accessways

(1)	An accessway must comply with AS 1428.2.

(2)	If an accessway branches into 2 or more parallel tracks:

(a)	the ends of each track must be on the main pedestrian traffic routes; and

(b)	the parallel tracks must have equal convenience and be located as close as practicable to the main pedestrian branch.

(3)	The minimum unobstructed width of an accessway must be 1.2 m, except that:

(a)	the minimum unobstructed width of a moving walkway forming part of an accessway may be not less than 850 mm; and

(b)	the minimum unobstructed width of a doorway in an accessway may be not less than 850 mm.

(4)	Poles, columns, stanchions, bollards and fixtures must not project into an accessway.

(5)	Obstacles that abut an accessway must have a luminance contrast with a background of not less than 30%.

(6)	Manoeuvring areas that allow a 180 degree wheelchair turn must comply with clause 6.2 of AS 1428.2.

(7)	A passing area must be provided at least every 6 metres along any twoway accessway that is less than 1 800 mm wide.

(8)	Ground and floor surfaces must comply with clause 9 of AS 1428.2 and AS 1428.1. Supplement 1 provides criteria for the selection of floor surfaces.

(9)	The requirements of subparagraph D3.3 (c) (ii) do not apply to Class 9b or Class 10 public transport buildings.

- Appendix A – Acronyms, abbreviations and glossary

| ARA | Australian Railway Association |
| --- | --- |
| DeoP | Down end of Platform |
| DTP | Department of Transport and Planning - The Victorian government department responsible for the delivery and planning of new and upgraded transport infrastructure and the ongoing operation and coordination of the State’s transport networks. |
| FA | Franchise Agreement |
| Flange Gap | Gap between the steel rail track and the road or surrounding pavement that permits train wheels to safely travel through level crossings. Flange gaps are required at level crossings to allow a train’s wheels to pass without obstruction. |
| HCMT | High Capacity Metro Trains |
| Level Crossing | An intersection where a railway line crosses a road or path at the same level. |
| Local Station | A Station that typically does not include staff other than Protective Services Officers in the evenings. |
| LXM | Level Crossing Management System |
| LXRP | Level Crossing Removal Project (formerly known as Level Crossing Removal Authority) |
| Metro/MTM | Metro Trains Melbourne |
| Premium Station | A Station that has passenger service staff during all timetabled operational hours and Protective Services Officers in the evenings. |
| RBP | Raised Boarding Pad |
| SME | Subject Matter Expert - An experienced person, nominated by the discipline Head of Engineering and/or Engineering Manager, who has the capability to provide expertise on a particular subject. |
| Network | Melbourne metropolitan railway network |
| Type Approval | Products installed on the Metropolitan Rail Network must be approved for use prior to being installed and commissioned. A list of products approved by MTM is detailed within the Approved Engineering Product List. If a product does not exist within the AEPL it must be approved for use by following the MTM Type Approval Procedure. |
| UeoP | Up end of Platform |

- Appendix B – Pedestrian crossings forming part of station access paths where flange gaps at level crossings are identified as non-compliant

| No | Station | Train Line | Pedestrian Crossing Name | Rail Chainage | Pedestrian Crossing Description |
| --- | --- | --- | --- | --- | --- |
| 1 | Clifton Hill | Mernda Line | Ramsden St | 6.42 | Up Footpath |
| 2 | Merri | Mernda Line | UeoP MERRI | 7.962 | Footpath |
| 3 | Northcote | Mernda Line | Charles St | 8.189 | Up Footpath |
|  |  |  | Arthurton Rd | 9.059 | Up Footpath |
| 4 | Croxton | Mernda Line | Beaconsfield Pde | 9.532 | Footpath |
|  |  |  | Gadd St | 9.701 | Footpath |
| 5 | Thornbury | Mernda Line | Hutton St | 10.551 | Up Footpath |
|  |  |  | DeoP THORNBURY | 10.7 | Footpath |
| 6 | Regent | Mernda Line | UeoP REGENT (Stewart St) | 13.529 | Footpath |
|  |  |  | Deop REGENT (Wild St) | 13.696 | Footpath |
| 7 | Keon Park | Mernda Line | Keon Pde | 17.442 | Up Left Footpath |
| 8 | Lalor | Mernda Line | Paschke Cr | 20.657 | Up Left Footpath |
| 9 | Westgarth | Hurstbridge Line | Westgarth St | 7.478 | Up Footpath |
| 10 | Dennis | Hurstbridge Line | Victoria Rd | 8.561 | Down Footpath |
| 11 | Fairfield | Hurstbridge Line | Station St | 9.253 | Up Footpath |
| 12 | Alphington | Hurstbridge Line | Yarralea St | 10.591 | Up Footpath |
| 13 | Macleod | Hurstbridge Line | DeoP MACLEOD | 17.786 | Footpath |
| 14 | Montmorency | Hurstbridge Line | UeoP MONTMORENCY | 24.668 | Footpath |
| 15 | Diamond Creek | Hurstbridge Line | UeoP DIAMOND CREEK | 32.574 | Footpath |
| 16 | Hurstbridge | Hurstbridge Line | UeoP HURSTBRIDGE | 37.825 | Footpath |
|  |  |  | DeoP HURSTBRIDGE | 38.092 | Footpath |
| 17 | Yarraville | Williamstown Line | Anderson St | 7.624 | Up Footpath |
| 18 | Spotswood | Williamstown Line | Hudsons Rd | 9.125 | Down Footpath |
| 19 | Seaholme | Werribee Line | Waratah St | 16.21 | Footpath |
| 20 | Altona | Werribee Line | Pier St | 17.057 | Up Footpath |
| 21 | Westona | Werribee Line | Maidstone St | 18.653 | Up Left Footpath |
| 22 | Keilor Plains | Sydenham Line | Ueop KEILOR PLAINS | 19.521 | Up Footpath |
| 23 | Diggers Rest | Sydenham Line | Old Calder Hwy | 32.813 | Footpath |
| 24 | Kensington | Craigieburn Line | Macaulay Rd | 3.5 | Up Footpath |
| 25 | Moonee Ponds | Craigieburn Line | Puckle St | 6.808 | Up Footpath |
| 26 | Pascoe Vale | Craigieburn Line | Gaffney St | 11.338 | Up Footpath |
| 27 | Craigieburn | Craigieburn Line | DeoP CRAIGIEBURN | 26.176 | Down Footpath - Right |
| 28 | North Melbourne | Upfield Line | Macaulay Rd | 3.188 | Up Footpath |
| 29 | Royal Park | Upfield Line | UeoP ROYAL PARK | 5.388 | Up Footpath |
| 30 | Jewell | Upfield Line | Barkly St | 6.406 | Footpath |
|  |  |  | Union St | 6.606 | Up Footpath |
| 31 | Brunswick | Upfield Line | Albert St | 7.212 | Up Footpath |
|  |  |  | Victoria St | 7.414 | Up Footpath |
| 32 | Anstey | Upfield Line | West St | 7.785 | Footpath |
|  |  |  | Albion St | 8.109 | Up Footpath |
| 33 | Batman | Upfield Line | Gaffney St | 11.097 | Up Footpath Left (East) |
| 34 | Merlynston | Upfield Line | DeoP MERLYNSTON | 12.562 | Footpath Left (East) |
| 35 | Fawkner | Upfield Line | DeoP FAWKNER | 13.272 | Down Footpath |
| 36 | Gowrie | Upfield Line | DeoP GOWRIE | 14.83 | 1 Footpath Left (East) |
| 37 | Upfield | Upfield Line | Barry Rd | 18.755 | Up Footpath |
| 38 | Narre Warren | Pakenham - Cranbourne Line | Webb St | 40.609 | Up Footpath |
| 39 | Berwick | Pakenham - Cranbourne Line | UeoP BERWICK | 44.63 | Footpath Left (Up Track) |
| 40 | Beaconsfield | Pakenham - Cranbourne Line | UeoP BEACONSFIELD | 46.91 | Footpath Right |
| 41 | Officer | Pakenham - Cranbourne Line | UeoP OFFICER | 51.384 | Footpath |
| 42 | Pakenham | Pakenham - Cranbourne Line | Main St | 58.023 | Down Footpath Left |
|  |  |  | UeoP PAKENHAM | 58.111 | Footpath |
| 43 | Prahran | Sandringham Line | Greville St | 6.67 | Up Footpath |
| 44 | Ripponlea | Sandringham Line | Glen Eira Rd | 9.912 | Up Footpath |
| 45 | North Brighton | Sandringham Line | Bay St | 13.324 | Up Footpath |
| 46 | Middle Brighton | Sandringham Line | Church St | 14.598 | Up Footpath |
| 47 | Brighton Beach | Sandringham Line | South Rd | 16.094 | Up Footpath |
| 48 | Hampton | Sandringham Line | Hampton St | 17.797 | Up Footpath |
| 49 | Sandringham | Sandringham Line | Abbott St | 19.004 | Up Footpath |
| 50 | Glenhuntly | Frankston Line | Glen Huntly Rd | 13.371 | Up Footpath Left |
| 51 | Highett | Frankston Line | Highett Rd | 20.14 | Up Footpath |
| 52 | Parkdale | Frankston Line | Alameda St/Bethell Ave | 25.815 | Footpath |
|  |  |  | Parkers Rd | 26.015 | Up Footpath |
| 53 | Mordialloc | Frankston Line | Mc Donald St | 27.583 | Down Footpath |
|  |  |  | Bear St | 27.802 | Up Footpath |
| 54 | Aspendale | Frankston Line | Groves Street | 30.411 | Up Footpath |
| 55 | Seaford | Frankston Line | Station St | 39.225 | Up Footpath |
| 56 | Frankston | Frankston Line | Beach St | 43.753 | Footpath |
| 57 | Somerville | Frankston Line | Pedestrian Crossing | 55.78 | Standalone |
| 58 | Tyabb | Frankston Line | Pedestrian Crossing | 59.904 | Standalone |
| 59 | Crib Point | Frankston Line | Disney St | 70.91 | Down Footpath |
| 60 | Kooyong | Glen Waverley Line | Glenferrie Rd | 8.201 | Up Footpath |
| 61 | Tooronga | Glen Waverley Line | UeoP TOORONGA | 9.514 | Up Footpath |
|  |  |  | Tooronga Rd | 9.754 | Up Footpath |
| 62 | Glen Iris | Glen Waverley Line | High St | 11.61 | Up Footpath Right |
| 63 | Riversdale | Alamein Line | Prospect Hill Rd | 11.515 | Down Footpath |
|  |  |  | Riversdale Rd | 11.87 | Down Footpath |
| 64 | Willison | Alamein Line | DeoP WILLISON | 12.239 | Footpath |
| 65 | Hartwell | Alamein Line | DeoP HARTWELL | 13.328 | Down Footpath (Right) |
| 66 | Burwood | Alamein Line | UeoP BURWOOD | 14.118 | Footpath |
| 67 | Ashburton | Alamein Line | DeoP ASHBURTON | 15.472 | Footpath |
| 68 | Heathmont | Belgrave Line | UeoP HEATHMONT | 28.023 | Footpath |
| 69 | Ferntree Gully | Belgrave Line | DeoP FERNTREE GULLY | 35.983 | DEOP Ferntree Gully |
| 70 | Upper Ferntree Gully | Belgrave Line | Hilltop Rd | 37.502 | Hilltop Rd Pedestrian Down |
| 71 | Ringwood East | Lilydale Line | UeoP EAST RINGWOOD | 27.754 | Right Footpath |
|  |  |  | DeoP EAST RINGWOOD | 27.874 | Footpath |
| 72 | Croydon | Lilydale Line | UeoP CROYDON | 30.961 | Footpath |
|  |  |  | Kent Av | 31.05 | Footpath |
| 73 | Lilydale | Lilydale Line | UeoP LILYDALE | 39 | Footpath |
|  |  |  | DeoP LILYDALE | 39.15 | Footpath |

- Appendix C – Stations with Curved Platforms

Station

Aircraft

Alamein

Albion

Alphington

Armadale

Ascot Vale

Beaconsfield

Belgrave

Berwick

Blackburn

Boronia

Box Hill

Burnley

Caulfield

Chatham

Clifton Hill

Coolaroo

Craigieburn

Cranbourne

Croxton

Darebin

Darling

Diamond Creek

Eaglemont

East Camberwell

East Malvern

East Richmond

Eltham

Epping

Essendon

Ferntree Gully

Flemington Racecourse

Flinders Street

Glen Iris

Glenbervie

Glenhuntly*

Hartwell

Hawksburn

Heidelberg

Heyington

Holmesglen

Hoppers Crossing

Jordanville

Kensington

Keon Park*

Kooyong

Laburnum

Lalor

Laverton

Lynbrook

Malvern

Middle Footscray

Moonee Ponds

Moorabbin

Mooroolbark

Mordialloc

Mount Waverley

Narre Warren

North Melbourne

Northcote

Nunawading

Oakleigh

Pakenham*

Pascoe Vale

Patterson

Richmond

Ringwood

Riversdale

Rushall

Ruthven

Sandown Park

Seaholme

Southern Cross

Stony Point

Strathmore

Syndal

Tecoma

Toorak

Tooronga

Tottenham

Upper Ferntree Gully

Upwey

Watergardens

Werribee

West Richmond

Westgarth

Westona

Williamstown

Willison

Yarraman

Frankston

* Planned accessibility upgrades

- Appendix D – DSAPT Section 6.4 Slope of external boarding ramps

Report of stations where 1 in 8 slope of external boarding ramp is not achieved.

| Burnley Group (Stations – Platforms) |
| --- |
| Glen Iris | Platform 2 |
| Darling | Platform 2 |
| East Malvern | Platform 1 |
| Glen Waverley | Platform 2 |
| Burnley | Platform 2 |
| Burnley | Platform 4 |
| Hawthorn | Platform 1 |
| Glenferrie | Platform 1 |
| Auburn | Platform 1 |
| Auburn | Platform 2 |
| Auburn | Platform 3 |
| Blackburn | Platform 2 |
| Croydon | Platform 2 |
| Ferntree Gully | Platform 2 |
| Upwey | Platform 1 |
| Upwey | Platform 2 |

| Central Group (Stations – Platforms) |
| --- |
| Flinders Street | Platform 7 |
| Flinders Street | Platform 12 |
| East Malvern | Platform 1 |
| Richmond | Platform 2 |
| Richmond | Platform 3 |
| Richmond | Platform 5 |
| Richmond | Platform 7 |
| Richmond | Platform 8 |
| Richmond | Platform 9 |

| Caulfield Group (Stations – Platforms) |
| --- |
| Hawksburn | Platform 1 |
| Hawksburn | Platform 2 |
| Toorak | Platform 1 |
| Toorak | Platform 2 |
| Toorak | Platform 4 |
| Malvern | Platform 4 |
| Yarraman | Platform 1 |
| Narre Warren | Platform 2 |
| Prahran | Platform 1 |
| North Brighton | Platform 1 |
| North Brighton | Platform 2 |
| Middle Brighton | Platform 1 |
| Middle Brighton | Platform 2 |
| Brighton Beach | Platform 2 |
| Brighton Beach | Platform 3 |
| Hampton | Platform 1 |
| Glen Huntly | Platform 2 |
| Mordialloc | Platform 1 |
| Mordialloc | Platform 2 |
| Kananook | Platform 2 |
| Bittern | Platform 1 |
| Mordialloc | Platform 1 |

| Northern Group (Stations – Platforms) |
| --- |
| Spotswood | Platform 1 |
| Newport | Platform 1 |
| Newport | Platform 2 |
| Williamstown | Platform 1 |
| Aircraft | Platform 1 |
| Middle Footscray | Platform 2 |
| Tottenham | Platform 2 |
| Flemington Racecourse | Platform 1 |
| Kensington | Platform 1 |
| Kensington | Platform 2 |
| Newmarket | Platform 2 |
| Moonee Ponds | Platform 1 |
| Essendon | Platform 2 |
| Essendon | Platform 3 |
| Strathmore | Platform 1 |
| Strathmore | Platform 2 |
| Pascoe Vale | Platform 2 |
| Oak Park | Platform 1 |
| Broadmeadows | Platform 2 |
| North Melbourne | Platform 5 |
| Royal Park | Platform 1 |
| Royal Park | Platform 2 |
| Jewell | Platform 2 |
| Anstey | Platform 1 |
| Coburg | Platform 1 |
| Batman | Platform 1 |
| Gowrie | Platform 1 |

| Clifton Hill Group (Stations – Platforms) |
| --- |
| West Richmond | Platform 1 |
| West Richmond | Platform 2 |
| Merri | Platform 1 |
| Regent | Platform 2 |
| Ivanhoe | Platform 2 |
| Heidelberg | Platform 1 |
| Watsonia | Platform 1 |